## Slide 1: SMARK AIR

## Slide 2: Table of Contents 01 04 02 05 06 03
About the Project
Who is the team?
What is this project?
Hardware/Software
What did we use and what did we create?
Project Goals
How do we determine the Project's success?
What next?
If we were to continue the project what would we do?
Retrospective
Were we succesful?
Project Sprints
What did we accomplished in each Sprint?

## Slide 3: Our Team
Curtis Ellenton
Hardware Programmer
John Narte
Hardware Programmer
Sam Nixon
Project Manager
Nathon Anderson
Software Developer
Frankie Ha
Software Developer
Jordan Caraiman
Software
Developer

## Slide 4: Air Quality Project
A comprehensive system that continuously monitors and analyzes the indoor air quality using sensors to accurately measure a range of critical environmental parameters including carbon dioxide (CO2) levels, temperature, humidity, as well as additional pollutants like volatile organic compounds (VOCs) and particulate matter (PM2.5 and PM10).

## Slide 5: Project Goals
Affordability
Useability
Portability

## Slide 6: Project Stages
Sprint 2
Hardware Programmed
And Website Core Features
Sprint 1
Procurement and Website Development
Sprint 3
Document Creation and all development finalized
All Stages
Final Product Achieved

## Slide 7: Current Hardware
Raspberry Pi 3b – $50.00
Enviro + Air Quality $69.95
PMS5003 sensor $15.59
GPS sensor - $20.00

## Slide 8: Future Hardware
Raspberry Pi Zero 2 W
Enviro + Air Quality
PMS5003 Sensor
Battery
Enclosure
New GPS sensor

## Slide 9: Sensor Code Overview
Key Functions
‘getGas()’: Reads MICS6814 Gas Sensor data
‘getWeather()’: Reads BME 280 Sensor data
‘getParticulates()’: Reads PMS5003 Particulate Sensor data
‘sendData()’: Transmits compiled data to the “smarkair.com” API
Implementation Details
CPU temperature compensation applied for more accurate surrounding temperature readings
Code gathers data 10 times every 5 seconds before transmitting data to the API

## Slide 10: Data Collection
BME 280
Sensor
Temperature
Pressure
Humidity
PMS5003 Particulate Matter Sensor
PM1.0
PM2.5
PM10
MICS6814 Gas Sensor
Oxidizing
Reducing
NH3
GPS
Sensor
Latitude
Longitude

## Slide 11: Hosting
MySQL Database
Part of Amazon Lightsail, it is a highly available, managed database allowing scalability and integrated tools such as backup and security settings
AWS Lightsail
Simplified cloud computing with easy setup. Launch websites, apps, and databases quickly and cost-effectively without complex infrastructure management
Cloudflare
Empowering websites with speed, security, and reliability. A global network optimizing performance and protecting against online threats seamlessly

## Slide 12: Database
High Availability databases
We have opted for High-availability plan databases, which are established in an extra Availability Zone to enhance stability and redundancy

## Slide 13: Source Code Management
To better manage our source code a GitHub repository was created for better organization and better collaboration.
GitHub

## Slide 14: Future Features
User’s will be able to see their device location and data on a webpage made with a google maps API key.
Adding Secondary Devices
User’s can add more devices to their Smark Air account.
Geolocation Webpage
Mobile App
Users can access data through the mobile app, and the webpage. Notifications will be sent via the app, not email

## Slide 15: Retrospective

## Slide 16: Demo

## Slide 18: Applied Security Measures
Cloudflare
Cloudflare safeguards websites through a multi-layered approach to security. Its global network provides DDoS protection, mitigating malicious traffic and ensuring website availability. The Web Application Firewall (WAF) filters out common web application attacks, while free SSL/TLS certificates encrypt data in transit. Cloudflare's CDN accelerates content delivery globally, reducing latency and improving performance. Bot management distinguishes between legitimate and malicious bots, and DNS security features protect against various DNS-related threats. Rate limiting, access control, and an Always Online feature further contribute to a robust defense against cyber threats, making Cloudflare an integral part of comprehensive website security.
Disable public mode of the database on AWS
Disabling public access to your AWS database provides a crucial security advantage by minimizing the risk of unauthorized access and potential exploits. This approach enhances network isolation, reduces the attack surface, and helps meet compliance standards. It prevents unauthorized connections, mitigates the risk of denial-of-service attacks, and allows for cost optimization by controlling data transfer. Additionally, secure access can be maintained through VPN or DirectConnect, enabling customized security controls and facilitating easier auditability of database access. Overall, this measure strengthens the database's security posture, protecting sensitive data from potential threats.